## Slide 1: Comparative vibration Test (Junker Test)

## Slide 2: Comparative Junker Test
1. Description of the test
Vibration tests (Junker test) for evaluating locking performance of Original SCHNORR® safety washers M8 made of carbon steel/spring steel (DIN EN 10132-4) with zinc-flake coating as well as tests of a competitors products for performance comparison
2. Reference standards of the test
The tests were based on the following reference standards:
- DIN 25201-4:2010-03 design guide for railway vehicles and their components – Bolted joints – Part 4: Securing of bolting joints – Appendix B
- DIN 65151:2002-08 Aerospace series – Dynamic testing of the locking characteristics of fasteners under transverse loading conditions (vibration test)
3. Test parameters and test implementation
Setting trials: Before testing, the setting trials were implemented according to the requirements of point B.3 of the DIN 25201-4. Flat washers according to DIN EN ISO 7093-1 were used as counter surface.
Vibration frequency used in tests: The frequency of the traverse displacements used was 12,5 Hz.
Preload and lubrication: The tested sets were tightened by wrench until the required preload corresponding to table B.1 of the DIN 25201-4 was reached. For the objects made of carbon/spring steel (DIN EN 10132-4) screws M8 in quality 8.8 were used, with a preload of Fvv of 9,1 kN. The tested sets were lubricated according to part B.5.2 of the DIN 25201-4 with lubrication-oil HD 30.

## Slide 3: Overview of the tested bolt locking systems
Product | Surface
Original SCHNORR® Safety Washers | Zinc-Flake
Wedge-Locking Washers | Zinc-Flake
Split Lock Washer | Mechanically galvanized
Detent-Eedged Washer | Zinc-Flake
Ripped Washer | Zinc-Flake
Spring Washer (DIN 137 B) | Mechanically galvanized

## Slide 4: Original SCHNORR® Safety Washer

## Slide 5: Overview competing products
Wedge-Locking Washers
Split Lock Washers
Detent-Edge Washers
Ripped Washers
Spring Washer
(DIN 137 B)

## Slide 6: Vibration Test result Original SCHNORR® safety washers (Art.-No. 401070)
Chart: Number of cycles
| 0 | 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650 | 700 | 750 | 800 | 850 | 900 | 950 | 1000 | 1050 | 1100 | 1150 | 1200 | 1250 | 1300 | 1350 | 1400 | 1450 | 1500 | 1550 | 1600 | 1650 | 1700 | 1750 | 1800 | 1850 | 1900 | 1950 | 2000
Original SCHNORR® safety washer 1 | 9.1 | 8.75 | 8.65 | 8.575 | 8.5 | 8.47 | 8.45 | 8.42 | 8.4 | 8.38 | 8.36 | 8.33 | 8.3 | 8.28 | 8.26 | 8.23 | 8.2 | 8.19 | 8.17 | 8.16 | 8.15 | 8.14 | 8.135 | 8.13 | 8.125 | 8.12 | 8.118 | 8.113 | 8.1 | 8.09 | 8.07 | 8.06 | 8.05 | 8.04 | 8.035 | 8.03 | 8.025 | 8.02 | 8.015 | 8.0075 | 8
Original SCHNORR® safety washer 2 | 9.1 | 8.55 | 8.38 | 8.29 | 8.205 | 8.125 | 8.05 | 8 | 7.95 | 7.925 | 7.9 | 7.875 | 7.85 | 7.825 | 7.8 | 7.775 | 7.75 | 7.74 | 7.725 | 7.718 | 7.7 | 7.685 | 7.675 | 7.669 | 7.65 | 7.6333 | 7.6167 | 7.609 | 7.6 | 7.59 | 7.58 | 7.57 | 7.565 | 7.56 | 7.55 | 7.54 | 7.535 | 7.53 | 7.52 | 7.51 | 7.5

## Slide 7: Prints of the Original SCHNORR® Safety Washers 401070
Prints are very well marked on the counter piece, which guarantees a high locking performance of the bolt

## Slide 8: Vibration Test results Comparison of Original SCHNORR® Safety Washers vs. Wedge-Locking Washer
Chart: Number of cycles
| 0 | 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650 | 700 | 750 | 800 | 850 | 900 | 950 | 1000 | 1050 | 1100 | 1150 | 1200 | 1250 | 1300 | 1350 | 1400 | 1450 | 1500 | 1550 | 1600 | 1650 | 1700 | 1750 | 1800 | 1850 | 1900 | 1950 | 2000
Original SCHNORR® Safety Washer | 9.1 | 8.75 | 8.65 | 8.575 | 8.5 | 8.47 | 8.45 | 8.43 | 8.4 | 8.38 | 8.36 | 8.33 | 8.3 | 8.28 | 8.26 | 8.23 | 8.2 | 8.19 | 8.17 | 8.16 | 8.15 | 8.14 | 8.135 | 8.13 | 8.125 | 8.12 | 8.118 | 8.113 | 8.1 | 8.09 | 8.07 | 8.06 | 8.05 | 8.04 | 8.035 | 8.03 | 8.025 | 8.02 | 8.015 | 8.0075 | 8
Nord-Lock | 9.1 | 8.2 | 8 | 7.95 | 7.9 | 7.88 | 7.86 | 7.83 | 7.8 | 7.76 | 7.73 | 7.69 | 7.65 | 7.63 | 7.6 | 7.58 | 7.53 | 7.51 | 7.48 | 7.465 | 7.45 | 7.44 | 7.425 | 7.41 | 7.4 | 7.39 | 7.385 | 7.38 | 7.375 | 7.37 | 7.365 | 7.3575 | 7.35 | 7.345 | 7.34 | 7.335 | 7.32 | 7.31 | 7.305 | 7.302 | 7.3
Twin-Lock | 9.1 | 8.5 | 8.32 | 8.22 | 8.15 | 8.1 | 8.066 | 8.025 | 8 | 7.9875 | 7.975 | 7.9625 | 7.95 | 7.9375 | 7.925 | 7.9125 | 7.9 | 7.8875 | 7.875 | 7.8625 | 7.85 | 7.8375 | 7.825 | 7.8125 | 7.8 | 7.7875 | 7.775 | 7.7625 | 7.75 | 7.7375 | 7.725 | 7.7125 | 7.7 | 7.6875 | 7.675 | 7.6625 | 7.65 | 7.6375 | 7.625 | 7.6125 | 7.6
Heico-Lock | 9.1 | 8.5 | 8.35 | 8.275 | 8.2 | 8.15 | 8.1 | 8.05 | 8 | 7.96 | 7.93 | 7.9 | 7.875 | 7.845 | 7.825 | 7.8 | 7.75 | 7.74 | 7.725 | 7.71 | 7.7 | 7.68 | 7.65 | 7.635 | 7.625 | 7.61 | 7.59 | 7.57 | 7.55 | 7.54 | 7.5275 | 7.515 | 7.5 | 7.48 | 7.465 | 7.4575 | 7.45 | 7.44 | 7.4275 | 7.415 | 7.4

## Slide 9: Vibration Test results Comparison of Original SCHNORR® Safety Washers vs. Split Lock Washer
Chart: Number of cycles
| 0 | 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650 | 700 | 750 | 800 | 850 | 900 | 950 | 1000 | 1050 | 1100 | 1150 | 1200 | 1250 | 1300 | 1350 | 1400 | 1450 | 1500 | 1550 | 1600 | 1650 | 1700 | 1750 | 1800 | 1850 | 1900 | 1950 | 2000
Original SCHNORR® Safety Washer | 9.1 | 8.75 | 8.65 | 8.575 | 8.5 | 8.47 | 8.45 | 8.43 | 8.4 | 8.38 | 8.36 | 8.33 | 8.3 | 8.28 | 8.26 | 8.23 | 8.2 | 8.19 | 8.17 | 8.16 | 8.15 | 8.14 | 8.135 | 8.13 | 8.125 | 8.12 | 8.118 | 8.113 | 8.1 | 8.09 | 8.07 | 8.06 | 8.05 | 8.04 | 8.035 | 8.03 | 8.025 | 8.02 | 8.015 | 8.0075 | 8
Split-Lock | 9.1 | 8.45 | 7.95 | 7.5 | 7.15 | 6.85 | 6.55 | 6.25 | 6 | 5.8 | 5.6 | 5.5 | 5.425 | 5.35 | 5.25 | 5.2 | 5.15 | 5.075 | 5 | 4.975 | 4.95 | 4.925 | 4.9 | 4.875 | 4.85 | 4.825 | 4.8 | 4.775 | 4.75 | 4.725 | 4.7 | 4.675 | 4.65 | 4.625 | 4.6 | 4.575 | 4.55 | 4.525 | 4.5 | 4.475 | 4.475

## Slide 10
Vibration Test results Comparison of Original SCHNORR® Safety Washers vs. Detent-Edged Washer
Chart: Number of cycles
| 0 | 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650 | 700 | 750 | 800 | 850 | 900 | 950 | 1000 | 1050 | 1100 | 1150 | 1200 | 1250 | 1300 | 1350 | 1400 | 1450 | 1500 | 1550 | 1600 | 1650 | 1700 | 1750 | 1800 | 1850 | 1900 | 1950 | 2000
Original SCHNORR® Safety Washer | 9.1 | 8.75 | 8.65 | 8.575 | 8.5 | 8.47 | 8.45 | 8.43 | 8.4 | 8.38 | 8.36 | 8.33 | 8.3 | 8.28 | 8.26 | 8.23 | 8.2 | 8.19 | 8.17 | 8.16 | 8.15 | 8.14 | 8.135 | 8.13 | 8.125 | 8.12 | 8.118 | 8.113 | 8.1 | 8.09 | 8.07 | 8.06 | 8.05 | 8.04 | 8.035 | 8.03 | 8.025 | 8.02 | 8.015 | 8.0075 | 8
detent-edged washer | 9.1 | 8.4 | 7.95 | 7.7 | 7.45 | 7.25 | 7.05 | 6.9 | 6.75 | 6.65 | 6.5 | 6.4 | 6.25 | 6.1 | 5.9 | 5.6 | 5.2 | 4.75 | 4.45 | 4.25 | 4 | 3.75 | 3.5 | 3.225 | 3 | 2.8 | 2.5 | 2.25 | 2 | 1.75 | 1.5 | 1.25 | 1 | 0.55 | 0

## Slide 11
Vibration Test results Comparison of Original SCHNORR® Safety Washers vs. Ripped Washer
Chart: Number of cycles
| 0 | 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650 | 700 | 750 | 800 | 850 | 900 | 950 | 1000 | 1050 | 1100 | 1150 | 1200 | 1250 | 1300 | 1350 | 1400 | 1450 | 1500 | 1550 | 1600 | 1650 | 1700 | 1750 | 1800 | 1850 | 1900 | 1950 | 2000
Original SCHNORR® Safety Washer | 9.1 | 8.75 | 8.65 | 8.575 | 8.5 | 8.47 | 8.45 | 8.43 | 8.4 | 8.38 | 8.36 | 8.33 | 8.3 | 8.28 | 8.26 | 8.23 | 8.2 | 8.19 | 8.17 | 8.16 | 8.15 | 8.14 | 8.135 | 8.13 | 8.125 | 8.12 | 8.118 | 8.113 | 8.1 | 8.09 | 8.07 | 8.06 | 8.05 | 8.04 | 8.035 | 8.03 | 8.025 | 8.02 | 8.015 | 8.0075 | 8
RIPP-Lock | 9.1 | 8.1 | 7.8 | 7.5 | 7.3 | 7.05 | 6.9 | 6.75 | 6.6 | 6.5 | 6.4 | 6.3 | 6.2 | 6.08 | 5.9 | 5.68 | 5.3 | 4.85 | 3.9 | 3.1 | 2.1 | 1.5 | 1.1 | 0.8 | 0.5 | 0.25 | 0

## Slide 12: Vibration Test results Comparison of Original SCHNORR® Safety Washers vs. Spring Washer
Chart: Number of cycles
| 0 | 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650 | 700 | 750 | 800 | 850 | 900 | 950 | 1000 | 1050 | 1100 | 1150 | 1200 | 1250 | 1300 | 1350 | 1400 | 1450 | 1500 | 1550 | 1600 | 1650 | 1700 | 1750 | 1800 | 1850 | 1900 | 1950 | 2000
Original SCHNORR® Safety Washer | 9.1 | 8.75 | 8.65 | 8.575 | 8.5 | 8.47 | 8.45 | 8.43 | 8.4 | 8.38 | 8.36 | 8.33 | 8.3 | 8.28 | 8.26 | 8.23 | 8.2 | 8.19 | 8.17 | 8.16 | 8.15 | 8.14 | 8.135 | 8.13 | 8.125 | 8.12 | 8.118 | 8.113 | 8.1 | 8.09 | 8.07 | 8.06 | 8.05 | 8.04 | 8.035 | 8.03 | 8.025 | 8.02 | 8.015 | 8.0075 | 8
Federscheibe | 9.1 | 8.6 | 8.1 | 7.65 | 6.95 | 5.8 | 2.9 | 1 | 0

## Slide 13: Comparison Original SCHNORR® safety washers and misc. bolt locking systems

## Slide 14: Résumé
The Junker test clearly shows a superior locking performance of the Original Schnorr® safety washers in term of number of cycles lasted and in term of residual spring load after 2000 cycles in comparison to split lock washers, detent-edged washer, ripped washers and spring washers (DIN 137 B)
The test also shows that Original Schnorr® safety washers have the same locking performance as all kinds of multifunctional wedge-locking washers just like Nord-Lock, Twin-Lock and Heico-Lock.